## Slide 1: Hydrogen production and CCS H21 North of England Henrik Solgaard Andersen – H21 Project Manager
Bryan Lovell Meeting 2019 - London

## Slide 2: Decarbonising Energy Systems
Transport
complexity to decarbonise
Easy
Hard
Power
Industry
Heat
Natural Gas Reforming to Hydrogen with CCS
Multiple technologies to address the challenge
Large Battery
Systems
for Daily Swing (night-to-day)
Hydro-Power as
Battery for Small Scale Intermittency
Hydrogen fired CCGTs
Clean Back-Up Power
for Large Scale Intermittency
Hydrogen
Fuel-Cell
Trains
Battery (mostly)
plus Hydrogen for Heavy Duty
Liquid Hydrogen
and Fuel-Cells for long haul Big Ships
Light Industry powered by Renewable
Heavy Industry powered by Hydrogen from Natural Gas + CCS
CCS for
Industry
without other
Alternatives
Heat Pumps
For Efficient Use of
Electricity in Homes
Hydrogen for
Large Scale Seasonal
Storage
Hydrogen for
Efficient Transfer of Energy from Production to End-Users

## Slide 3: Understanding the Challenge
Vehicle
Battery park
Hydro
20 000 000 000 X
11,600,000 x
HYDROGEN to Heat
HYDROGEN to Power Generation
New Projects
TESLA 75D Li-Batteries
Norways biggest hydro electrical storage -Blåsjø
World largest
battery park in Australia (129 MWh)
11 600 000 X
200 X
Natural Gas currently provides Europe with more than 1500 TWh of inter seasonal flexible energy.
What is 1500 TWh?

## Slide 4: CCS as enabler for hydrogen production
Clean Hydrogen
H2
        for power generation
        for heat
        for maritime transport
Natural Gas
CO2
H2

## Slide 5
Natural Gas Reforming with CCUS hydrogen supply chains
Proven and referenced technology at scale (TWh-solutions)
Build and commissioned at mega scale
95% CO2 reduction equal to a CO2 footprint of 14-15 g/kWh
Robust and reliable design to meet customers demand
Can deliver credible CO2 reductions for 2030 and 2050 targets
Building upon a strong existing large scale industry

## Slide 6: H21 North of England – Meeting the Climate Change Act 2008 based on proven and referenced technology
Key Features
Conversion start 2028 with stepwise expansion to 2035 replacing more than 3.7 million appliances
Resilient design to fulfil security of supply during peak winter (the beast from the east)
Design capacity of 85 TWh
12.5 million CO2 per year avoided
12.1 GW hydrogen production in UK based on reforming of natural gas with CCS
8 TWh inter seasonal hydrogen storage in salt caverns in UK
Offshore CO2 storage in either UK or Norway
CO2 footprint: 14.47 g/kWh

## Slide 7: H21 NoE Commissioning – Hydrogen Supply and CCS (Equinor part)
Greenfield Hydrogen Facility
Location: Easington
Capacity: 12.15 GW
Configuration: Modular design and self sufficient with power
CO2 Storage
Location: Bundter
Capacity: +600 Million @ 17 mtpa
Configuration: Saline aquifers
Hydrogen Storage
Location: Aldbrough
Capacity: 8 TWh
Configuration : 56 salt caverns at 300,000 m3

## Slide 8: Inter-Seasonal hydrogen storage: Commissioning
Salt caverns – best suited/multiple cycles - proven
Depleted oil/gas fieds and aquifers: Strategic storage 1-2 annual cycles – not proven
Allows for optimisation of production and storage capacity

## Slide 9: CO2 transport and storage: Commissioning and cost

## Slide 10: H21 NoE Commissioning – Transmission, distribution and appliances (NGN part)
Hydrogen Transport System
Pipeline length: 520 km
Capacity: 120 GW
Linepack for handling peak hour demand and daily swing

## Slide 11: H21 NoE – Cost and finance
Gas bill increase by 50% in a H21 all UK scenario or 25 £/MWh
BEIS 2035 electricity forecast : 200 £/MWh equal increase of 50 £/MWh

## Slide 12
UK’s theoretical CCS potential:
78,000 Million tonnes CO2
90 x H21 NoE in 50 years
6700 TWh/a of hydrogen
Decarbonise all European gas
Decarbonise all European road fuel
Annual revenue of £ 280 Bill
Creating millions of jobs and leading IP
Enabling the biggest market for green hydrogen and renewable energy
UK a future low carbon energy super power
- A potential for 6700 TWh/y of clean energy

## Slide 13: Low Carbon Solutions